PowerPoint Presentation
1st Law Closed System
Wout
Qout
Win
Qin
%DELTA E={%SIGMA Q -%SIGMA W} underbrace {}
Net change of system energy
Net total energy transfer in the form of heat and work

---
(ctd.)
- Recall that System Energy consists of:
Esistem= U + KE + PE
or
Esistem= U + KE + PE
thus;
Q – W = Esystem= U + KE + PE
Or can be called as the
1st Law/Energy Balance of a Closed System;
Q – W = U + KE + PE
Net transfer of energy
Energy storage in different modes

---
1st Law for Closed System in different forms;
Q – W = U + KE + PE	[kJ]
per unit mass;
q – w = u + ke + pe	[kJ/kg]
Rate form;
[kW]
Cyclic Process	E =0
Q-W=0 newline Q_cycle =W_cycle newline sum Q= sum W

---
summary;
mg(z2-z1)
m(u2-u1) water (Table)
mCv(T2-T1) ideal gas
Electrical
Mechanical
Boundary
etc…