Chap 3 Examples

A system undergoes a thermodynamic cycle following the sequence 1-2-1. Process 1-2 follows path A while process 2-1 follows path B. Heat and work transfers are determined to be W12= - 23 kJ, Q12= 11 kJ and W21= - 46 kJ. If the system energy at state 1, E1 is 32 kJ, calculate Q21.

Water in a piston cylinder device undergoes 2 processes in series. The initial state is 1 MPa, 400 oC.
Process 1 – 2 : Water is cooled at constant pressure until it becomes saturated vapor at 1 MPa
Process 2- 3 : Water is cooled further at constant volume until the pressure reaches 0.5 MPa
Sketch the processes on the T-v and p-v diagrams. Determine total work and heat transfer.

2 kg of steam at 1 MPa is cooled at constant volume, V=0.45 m3, to the pressure of 0.5 MPa. It then expands at constant pressure until the volume reaches 0.95 m3. Determine the specific volume and specific internal energy at each state, and also the work and heat involved in the process. Sketch the p-v diagram of the processes.

1. Sebuah sistem silinder beromboh mengandungi udara pada 150 kPa dan 27 oC. Pada keadaan ini omboh terletak di atas sepasang penahan dan isipadu silinder ialah 400 L. Untuk menggerakkan omboh, tekanan 350 kPa diperlukan. Udara dipanaskan sehingga isipadunya bertambah dua kali ganda. Tentukan
  1. Suhu pada keadaan akhir
  2. Kerja dilakukan oleh udara
  3. Jumlah haba yg dibekalkan kepada udara

3 kg udara menjalani satu kitar termodinamik yang terdiri dari 3 proses. Proses 1 ke 2 ialah pemampatan politropik dengan n = 1.2 dari keadaan awal 150 kPa, 360 K ke tekanan 750 kPa. Ia diikuti oleh penyejukan pada tekanan malar dari 2 ke 3. Ini dikuti pula oleh proses pemanasan sesuhu balik kepada keadaan asal.
Lakar rajah p-v­ kitar dan tentukan kerja dan haba setiap proses dan jumlah kerja dan haba kitaran.