PowerPoint Presentation
Steady Flow Process
Criteria;
All system properties (intensive & extensive) do not change with time
mcv= constant;	mCV= 0
VCV= constant; VCV= 0
ECV= constant;	ECV= 0
Fluid properties at all inlet/exit channels do not change with time (Values might be different for different channels)
Heat and work interactions do not change with time
dot Q = constant newline dot W = constant

---
Implication of Criterion 1
(Mass)
mCV= 0,
From Mass Conservation;
Recall that
so
for 1 inlet/ 1 exit;

---
(Volume)
VCV= 0,
	WB = 0	(boundary work = 0 )
ECV= Q – W + Eflow(in) - Eflow(out)
W = Welectrical + Wshaft + Wboundary+ Wflow+ Wetc.
0
in h
W not necessarily 0, only WB is 0